## Slide 1: F-bar aided Edge-based Smoothed Finite Element Method with Tetrahedral Elements for Large Deformation Analysis of Nearly Incompressible Materials
Yuki ONISHI Tokyo Institute of Technology (Japan)

## Slide 2: Motivation & Background
Motivation
  We want to analyze severe large deformation of nearly incompressible solids accurately and stably! (Target: automobile tire, thermal nanoimprint, etc.)
Background
  Finite elements are distorted in a short time, thereby resulting in convergence failure.
Mesh rezoning method (h-adaptive mesh-to-mesh solution mapping) is indispensable.
Mold
Polymer
1m

## Slide 3: Our First Result in Advance
What we want to do:
Static
Implicit
Large deformation
Mesh rezoning

## Slide 4: Issues
The biggest issue in large deformation mesh rezoning
It is impossible to remesh arbitrary deformed 3D shapes with hexahedral (H8) elements.
However, the standard (constant strain) T4 elements easily induce shear and volumetric locking, which leads to inaccurate results.
We have to use tetrahedral (T4) elements...

✗

## Slide 5: Conventional Methods
Higher order elements: ✗ Not volumetric locking free; Unstable in contact analysis; No good in large deformation due to intermediate nodes.
EAS method: ✗ Unstable due to spurious zero-energy modes.
B-bar, F-bar and selective integration method: ✗ Not applicable to T4 mesh directly.
F-bar patch method: ✗ Difficult to construct good patches. Not shear locking free.
u/p hybrid (mixed) elements: ✗ No sufficient formulation for T4 mesh so far. (There are almost acceptable hybrid elements such as C3D4H of ABAQUS.)
Smoothed finite element method (S-FEM): ? Unknown potential (since 2009~). It’s worth trying!!

## Slide 6: Various Types of S-FEMs
Basic type
  Node-based S-FEM (NS-FEM)
  Face-based S-FEM (FS-FEM)
  Edge-based S-FEM (ES-FEM)
Selective type
  Selective FS/NS-FEM
  Selective ES/NS-FEM
Bubble-enhanced or Hat-enhanced type
  bFS-FEM, hFS-FEM
  bES-FEM, hES-FEM
F-bar type
  F-barES-FEM
NEW
✗ Volumetric Locking
✗ Spurious zero-energy
✗ Limitation of constitutive model, Pressure oscillation, Corner locking
? Unknown potential
✗ Pressure oscillation, Short-lasting

## Slide 7: Objective
Develop a new S-FEM, F-barES-FEM-T4, by combining F-bar method and ES-FEM-T4 for large deformation problems of nearly incompressible solids
Table of Body Contents
Method: Formulation of F-barES-FEM-T4
Result: Verification of F-barES-FEM-T4
Summary

## Slide 8
Method
Formulation of F-barES-FEM-T4
(F-barES-FEM-T3 in 2D is explained for simplicity.)

## Slide 9: Quick Review of F-bar Method
Algorithm
Calculate deformation gradient at the element center, and then make the relative volume change .
Calculate deformation gradient at each gauss point as usual, and then make ) .
Modify at each gauss point as
.
Use to calculate the stress, nodal force and so on.
F-bar method is used to avoid volumetric locking in Q4 or H8 elements. Yet, it cannot avoid shear locking.
For quadrilateral (Q4) or hexahedral (H8) elements

## Slide 10: Quick Review of ES-FEM
Algorithm:
Calculate the deformation gradient at each element as usual.
Distribute the deformation gradient to the connecting edges with area weights to make at each edge.
Use to calculate the stress, nodal force and so on.
ES-FEM is used to avoid shear locking in T3 or T4 elements. Yet, it cannot avoid volumetric locking.
For triangular (T3) or tetrahedral (T4) elements.

## Slide 11: Outline of F-barES-FEM
Concept
is given by ES-FEM.
is given by Cyclic Smoothing (detailed later).
is calculated in the manner of F-bar method:
.
Combination of F-bar method and ES-FEM

## Slide 12: Outline of F-barES-FEM
Brief Formulation
Calculateas usual.
Smooth at nodes and get.
Smooth at elements and get.
Repeat 2. and 3. as necessary ( times).
Smooth at edges to make .
Combine and of ES-FEM as
.
Cyclic Smoothing of
Hereafter, F-barES-FEM-T4 with -time cyclic smoothing is called “F-barES-FEM-T4()”.
( layers of ~)

## Slide 13
Result
Verification of F-barES-FEM-T4
(Analyses without mesh rezoning are presented for pure verification.)

## Slide 14: #1: Bending of a Cantilever
Outline
Neo-Hookean hyperelastic material with a constant (=1 GPa) and various s so that the initial Poisson’s ratios are 0.49 and 0.499.
Two types of tetra meshes: structured and unstructured.
Compared to ABAQUS C3D4H (1st-order hybrid tetrahedral element).
Dead Load

## Slide 15: #1: Bending of a Cantilever
Pressure Distributions
ABAQUS C3D4H
F-bar ES-FEM- T4(1)
Structured Mesh

## Slide 16: #1: Bending of a Cantilever
Pressure Distributions
F-bar ES-FEM-
T4(2)
F-bar ES-FEM- T4(3)
Increase in the number of cyclic smoothing () makes stronger suppression of pressure oscillation.
Structured Mesh

## Slide 17: #1: Bending of a Cantilever
Pressure Distributions
ABAQUS C3D4H
F-bar ES-FEM- T4(1)
Unstructured Mesh

## Slide 18: #1: Bending of a Cantilever
Pressure Distributions
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(2)
No mesh dependency is observed.
Unstructured Mesh

## Slide 19: #2: Compression of a Block
Outline
Arruda-Boyce hyperelastic material ().
Applying pressure on ¼ of the top face.
Compared to ABAQUS C3D4H with the same unstructured tetra mesh.
Load

## Slide 20: #2: Compression of a Block
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(2)
Early stage Middle stage Later stage

## Slide 21: #2: Compression of a Block
Pressure Distribution
Early stage Middle stage Later stage
F-bar ES-FEM- T4(3)
F-bar ES-FEM- T4(4)
In case the Poisson’s ratio is 0.499, F-barES-FEM-T4(2) or later can suppress pressure oscillation successfully in large strain analysis.

## Slide 22: #3: Compression of 1/8 Cylinder
Outline
Neo-Hookean hyperelastic material ().
Enforced displacement is applied to the top surface.
Compared to ABAQUS C3D4H with the same unstructured tetra mesh.

## Slide 23: #3: Compression of 1/8 Cylinder
Result of F-bar ES-FEM(2)
50% nominal compression
Almost smooth
pressure
distribution is obtained
except just around the rim.

## Slide 24: #3: Compression of 1/8 Cylinder
Pressure Distribution
ABAQUS C3D4H
F-bar ES-FEM-
T4(3)
F-bar ES-FEM-
T4(4)
F-bar ES-FEM- T4(2)
F-barES-FEM-T4 with a sufficient cyclic smoothing also resolves the corner locking issue.

## Slide 25: Characteristics of F-barES-FEM-T4
Benefits
  Locking-free with tetra meshes.
  No increase in DOF; No need of static condensation; Easy extension to dynamic explicit analysis.
  No difficulty in contact analysis.
  Adjustable smoothing level by changing the number of cyclic smoothings ().
  Suppression of pressure oscillation in nearly incompressible materials.
  In point of accuracy, F-barES-FEM-T4 is excellent!!

## Slide 26: Characteristics of F-barES-FEM-T4
Drawbacks
  ✗ Blur of high-frequency pressure distribution. (The impact of blur seem to be not significant.)
  ✗ Increase in bandwidth of the exact tangent stiffness . In case of standard unstructured T4 meshes,
  In point of speed, F-barES-FEM-T4 needs some improvements. e.g.) finding a good sparse approximation of for iterative matrix solvers.
Method | Approx. Bandwidth | Approx. Ratio
Standard FEM-T4 | 40 | 1
F-barES-FEM(1) | 390 | x10
F-barES-FEM(2) | 860 | x20
F-barES-FEM(3) | 1580 | x40
F-barES-FEM(4) | 2600 | x65

## Slide 27
Summary

## Slide 28: Summary
A new FE formulation named “F-barES-FEM-T4” is proposed.
F-barES-FEM-T4 combines the F-bar method and ES-FEM-T4.
Owing to the cyclic smoothing, F-barES-FEM-T4 is locking-free and also pressure oscillation-free with no increase in DOF.
Only one drawback of F-barES-FEM-T4 is the decrease of calculation speed due to the increase in bandwidth of , which is our future work to solve.
Thank you for your kind attention!

## Slide 29
Appendix

## Slide 30: Characteristics of FEM-T4s
 | Shear & Volumetric Locking | Zero- Energy Mode | Dev/Vol Coupled Material | Pressure Oscillation | Corner Locking | Severe Strain
Standard FEM-T4 | ✗ |  |  | ✗ | ✗ | 
ABAQUS C3D4H |  |  |  | ✗ | ✗ | 
Selective S-FEM-T4 |  |  | ✗ | ✗ | ✗ | 
bES-FEM-T4 hES-FEM-T4 |  |  |  | ✗ | ✗ | ✗
F-bar ES-FEM-T4 |  |  |  | * | * | 
) when the num. of cyclic smoothings is sufficiently large.
*

## Slide 31: #3: Compression of 1/8 Cylinder
Result of F-bar ES-FEM(2)
Smooth
Mises stress
distribution is obtained
except just around the rim.
50% nominal compression