## Slide 1: Performance of Smoothed Finite Element Methods with Tetrahedral Elements in Large Deformation Elasto-Plastic Analysis
Yuki ONISHI Tokyo Institute of Technology, Japan

## Slide 2: Motivation
Motivation
  We want to accurately and stably analyze severe large deformation of solids in any shape with finite elements.
Issues
  Severe large deformation of arbitrary body No Hex mesh. Only Tet mesh.
  1st order standard tetrahedral (constant strain) element (e.g. C3D4 in ABAQUS) for materials with incompressibility Shear/volumetric locking and pressure oscillation.
  2nd order u/p hybrid tetrahedral element (e.g., C3D10H, C3D10MH in ABAQUS) Low accuracy in severe large deformation. Convergence difficulty in contact.
  Researches on FE formulations for 1st order tetra (T4) are still active especially for rubber-like or elasto-plastic materials.

## Slide 3: An Example for Rubber-like Material
Material: neo-Hookean hyperelastic,
1st order hybrid T4 (C3D4H)  No shear/volumetric locking
✗ Pressure oscillation
✗ Corner locking
2nd order modified hybrid T10 (C3D10MH)
 No shear/volumetric locking
✗ Decrease in interpolation accuracy ✗ Early convergence failure
# of Nodes is almost the same.
Pressure
Pressure

## Slide 4: An Example for Rubber-like Material
Material: neo-Hookean hyperelastic,
F-barES-FEM-T4 (a new type of smoothed finite element method (S-FEM))  No shear/volumetric locking
 Less pressure oscillation  Less corner locking
F-barES-FEM-T4 has excellent accuracy on rubber-like materials.
How about it on elasto-plastic materials?
# of Nodes is exactly the same as the C3D4H case.

## Slide 5: Objective
Apply the new type of S-FEM, F-barES-FEM-T4, to large deformation problems of elasto-plastic materials.
Table of Body Contents
Methods: Quick introduction of F-barES-FEM-T4
Results: A few verification analyses
Summary

## Slide 6
Methods
Quick introduction of F-barES-FEM-T4 (F-barES-FEM-T3 in 2D is explained for simplicity.)

## Slide 7: What is S-FEM?
S-FEM: Smoothed Finite Element Method
A new sort of strain smoothing technique (since 2007).
Strain is smoothed across elements.
Various types of S-FEMs:
  Basic types
    Node-based S-FEM (NS-FEM)
    Face-based S-FEM (FS-FEM)
    Edge-based S-FEM (ES-FEM)
  Selective types (e.g. ES/NS-FEM)
  Bubble types (e.g. bES-FEM)
  F-bar type (e.g. F-barES-FEM)
✗ Spurious zero-energy mode or Volumetric locking, Pressure oscillation, Corner locking.
NEW
 Good in hyperelastic case. ? Unknown in elasto-plastic case.

## Slide 8: Quick Review of NS-FEM
Algorithm:
Calculate the deformation gradient at each element as usual.
Distribute the deformation gradient to the connecting nodes with area weights to make at each node.
Use to calculate the stress, nodal force and so on.
NS-FEM avoids shear/volumetric locking in T3/T4 elements. Yet, it suffers from zero-energy modes, pressure oscillation and corner locking...
For triangular (T3) or tetrahedral (T4) elements.

## Slide 9: Quick Review of ES-FEM
Algorithm:
Calculate the deformation gradient at each element as usual.
Distribute the deformation gradient to the connecting edges with area weights to make at each edge.
Use to calculate the stress, nodal force and so on.
ES-FEM avoids shear locking in T3/T4 elements. Yet, it suffers from volumetric locking, pressure oscillation and corner locking…
For triangular (T3) or tetrahedral (T4) elements.

## Slide 10: Quick Introduction of F-barES-FEM
is given by ES-FEM.
is given by cyclic nodal smoothing.
is calculated in the manner of F-bar method:
.
Concept: combination of F-bar method and ES-FEM

## Slide 11
Results
A few verification analyses

## Slide 12: Bending of Elasto-Plastic Spanner
P. 12
Outline
2 faces are perfectly constrained.
Pressure is applied to a side part of the spanner.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Fixed
Pressure
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
8.5 k nodes & 33 k elems.

## Slide 13: Bending of Elasto-Plastic Spanner
Equivalent Plastic Strain
Distributions of
equivalent plastic strain
are about the same.
ABAQUS C3D4H
F-barES-FEM-T4

## Slide 14: Bending of Elasto-Plastic Spanner
F-barES-FEM-T4
Pressure
ABAQUS C3D4H
ABAQUS C3D4H suffers from pressure oscillation even in a small deformation elasto-plastic case.
Checkerboard patterns here.
Smooth distribution here.

## Slide 15: Shearing & Tensioning of Elasto-Plastic Bar
P. 15
Outline
Blue face is perfectly constrained.
Red face is constrained in plane and pressed down.
Compared to ABAQUS C3D4H with the same unstructured T4 mesh.
Elasto-plastic material:
Hencky elasticity with and .
Isotropic von Mises yield criterion with and (constant).
1.2 k nodes & 4.8 k elems.

## Slide 16: Shearing & Tensioning of Elasto-Plastic Bar
Result of F-bar ES-FEM (Equiv. Plastic Strain)

## Slide 17: Shearing & Tensioning of Elasto-Plastic Bar
P. 17
Equivalent Plastic Strain
F-barES-FEM-T4
ABAQUS C3D4H
There is minor oscillation.
Smooth distribution.

## Slide 18: Shearing & Tensioning of Elasto-Plastic Bar
P. 18
Equivalent Plastic Strain
F-barES-FEM-T4
ABAQUS C3D4H
Accuracy of equivalent plastic strain seems no much different.

## Slide 19: Shearing & Tensioning of Elasto-Plastic Bar
P. 19
Pressure
F-barES-FEM-T4
ABAQUS C3D4H
Smooth distribution.
There is major oscillation.

## Slide 20: Shearing & Tensioning of Elasto-Plastic Bar
P. 20
Pressure
Accuracy of pressure is quite different due to the pressure oscillation of ABAQUS C3D4H.
F-barES-FEM-T4
ABAQUS C3D4H

## Slide 21
Summary

## Slide 22: Benefits and Drawbacks of F-barES-FEM-T4
Benefits
  Locking-free with 1st -order tetra meshes.
  No difficulty in severe strain or contact analysis.
  No increase in DOF.
  No intermediate nodes. No need for static condensation.
  No restriction of material constitutive model. Pressure dependent models are acceptable.
  Less pressure oscillation and corner locking.
Drawbacks
✗ The more cyclic smoothing necessitates the more CPU time.

## Slide 23: The Take-Home Message
  If you are interested in elasto-plastic problems that have
    3D bulk complex shapes,
    severe large deformation or contact, and especially
    pressure dependent constitutive models,
  then, please consider using F-barES-FEM-T4.
Thank you for your kind attention!